JSC Mozyr Oil Refinery

The Republic of Belarus, Gomel Region, 247760, Mozyr-11

Passport No 26

Methyl tert butyl ether (MTBE), Grade A

Technical Specification BY 400091131.012-2017

Lot No 26

Gross weight           kg                            Net weight                       kg

Production date 21.08.2019

Tank No36

Measurement 375

| No | Name of parameter | Unit | Test method | Limits as per Tech. specification BY 400091131.0001-2008 | Factual |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Min. | Max. |  |
| 1 | Appearance |  | As per cl. 4.3 Tech. spec. BY 400091131.012 | Transparent liquid | transparent |
| 2 | Methyl tert butyl ether mass fraction | % | ASTM D5441 | 98,0 | - | 98,78 |
| 3 | Alcohol mass fraction (methanol and ter-butanol) | % | ASTM D5441 | - | 1,5 | 0,82 |
| 4 | Hydrocarbons (C₄ and С₈) mass fraction | % | ASTM D5441 | - | 1,5 | 0,8 |
| 5 | Water mass fraction | % | STB ISO 12937 | - | 0,15 | 0,022 |
| 6 | Sulphur mass fraction | Mg/kg | GOST ISO 20846 | - | 15 | 9 |
| 7 | Mechanical impurities | - | As per cl. 4.3 Tech. spec. BY 400091131.012 | absent | absent |
| 8 | Density at 15 º C | kg\m³ | STB ISO 12185-2007 | Not rated, determination is mandatory | 746,0 |

Conclusion: the product is as per standard and the quality corresponds to Technical Specification  400091131.012-2017.

The guarantee period: 1 year form the production date.

Additionally for customs clearance purposes for export deliveries: Methyl tert butyl ether (MTBE) is cyclic ether.

Senior laboratory technician: N.F. Leonovich		Date of passport issue: 21.08.2019