JSC Mozyr OR

Passport No1797

Fuel oil 100

Grade VI ashy

With setting temperature 25 ºC

GOST 10585-99

Gross weight          kg                 net weight          kg

Production date 17.09.2014

| No | Name of parameter | GOST value norm | Actually |
| --- | --- | --- | --- |
| 1 | Viscosity at 100 ºC, max conditional, degrees of CV or kinematic, m²\s | 50,0x10 (50,0) | 45,3 |
| 2 | Ash content, %, max for fuel oil: Low-ashy ashy | 0,05 0,14 | 0,1 |
| 3 | Mass fraction of mechanical impurities, %, max | 1,0 | 0,08 |
| 4 | Water mass fraction, %, max | 1,0 | Abs |
| 5 | Content of water-soluble acids and alkalies | abs | Abs |
| 6 | Sulfur mass fraction, %, max for fuel oils type: I II III IV V VI VII | 0,5 1,0 1,5 2,0 2,5 3,0 3,5 | 2,51 |
| 7 | Open-cup flash-point, ºC, min | 110 | 142 |
| 8 | Pour point , ºC, max for fuel oils produced from highly paraffinic crude | 25 42 | 10 |
| 9 | Combustion value(min) as converted for dry fuel (non-sorting), kJ\kg, min for fuel oil types: I,II,III,IV V,VI,VII | 40530 39900 | 40200 |
| 10 | Density at 20 ºC, kg\m³ | Not rated Estimation is mandatory | 987,8 |
| 11 | Content hydrogen sulfide and mercaptans, mg/kg, max | Abs | Abs |

Conclusion: the standard product corresponds to GOST 10585-99 requirements.