PASSPORT No 1147

OJSC Mozyr Refinery

Hydrotreated vacuum gasoil Type I (Specification TU BY 300220696.023-2004)

Produced: 09.08.2015

| No | Parameters description | Norm | Fact |
| --- | --- | --- | --- |
| 1 | Distillation: 10% distilled at, ºC, max 50% distilled at, ºC, max 90% distilled at, ºC, max | 405 460 530 | 387 444 516 |
| 2. | Density at 20 ºC, kg\m3, max | 910 | 893,3 |
| 3. | Flash point defined in open firepot, ºC, min | 160 | 186 |
| 4. | Kinematic viscosity at 50 ºC, mm2\sec, max | 32,0 | 25,50 |
| 5. | Pour point ºC, max | 41 | 34 |
| 6. | Sulfur mass fraction, %, max: Type I Type II Type III | 0,2 0,3 0,5 | 0,16 |
| 7. | Coking power, %, max | 0,2 | 0,17 |
| 8. | Vanadium mass fraction, %, max | 0,0005 | 0,00005 |