JSC Mozyr Oil Refinery

The Republic of Belarus, Gomel Region, 247760, Mozyr-11

Passport No 1252

High-octane gasoline component (alkylate)

Technical Specification BY 400091131.0001-2008

Lot No 1252

Gross weight           kg                            Net weight                       kg

Production date 28.08.2019

Tank No100\1

Measurement 965 cm

| No | Name of parameter | Unit | Test method | Limits as per Tech. specification BY 400091131.0001-2008 | Factual |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Min. | Max. |  |
| 1 | Density at 15 º C | kg\m³ | GOST 31072 | Not rated, determination is mandatory | 700,0 |
| 2 | Octane number, research method |  | GOST 32339 | 94,0 | - | 97,1 |
| 3 | Octane number, motor method |  | GOST 32340 | 91,0 | - | 95,0 |
| 4 | Distillation: Temperature of distillation beginning End of boiling Residue in a flask Residue + losses | ºC ºC % vol % vol | GOST ISO 3405 | 35,0 - - - | - 210 1,5 4,0 | 38 166 1,0 3,0 |
| 5 | Pressure of saturated vapors, DVPE | kPascal | STB EN 13016-1 | - | 60,0 | 38,4 |
| 6 | Sulphur content | Mg\kg | GOST ISO 20846 | - | 10,00 | 1,4 |
| 7 | Corrosion attack on copper plate for 3 hrs at 50 º C |  | STB ISO 2160 | Class 1 | Class 1 |
| 8 | Appearance |  | Visually | Clean and clear | Clean and clear |
| 9 | Volume fraction of hydrocarbons: Aromatic, Olefinic, | % % | STB 1276 | - - | 0,5 0,5 | 0,20 0,09 |
| 10 | Content of water and total impurities |  | As per cl. 4.2 Tech. spec. BY 400091131.001 | absent | absent |

Conclusion: the product is as per standard and the quality corresponds to Technical Specification  BY 400091131.0001-2008

The guarantee period: 1 year form the production date.

Additionally for customs clearance purposes for export deliveries:

Distillation % at 210 ºC (ASTM D86) – 97,0

Pentane (C5) content, % max. – 2,5

Hexane (C6) content, % max. 1,5

Chemist: L.M. Beresneva					Date of passport issue: 28.08.2019